| Experiment Proposal |
| --- |
| Title | Author/Spokesperson |
| Screen investigations with Slow extraction | A. Reiter (1431) B. Walasek-Höhne (1733) |
| Summary & Aim |
| R&D for FAIR: Test of screens with protons and light ions Investigation of several types of screen materials The measurements will be performed with slow extraction from HIT synchrotron. Requested beam time: 1 shifts Measured quantities: Absolute signal, linearity Test of DAQ & analogue electronics chain with FESA-compatible hardware Recorded data: Signals as function of particle number, beam width |
| Machine parameters |
| Machine HIT synchrotron, slow extraction Mode Exp. area QA room Ion species Protons & Light ions Beam energy Proton: up to 220 MeV Carbon: up to 430 MeV/u Spill length Several seconds Particle number 104 – 109 per spill Repetition rate few Hz Shifts 1 shifts Beam Time Period Q3/Q4 2013 Health & Safety No concerns |
| Experiment procedure |
| After setup of beam at end of QA beam line, the following series of data are taken: Screen signals (beam profiles) for different ion species and energies Investigation of linearity, light yield stability |

Experiment Setup

Exp. area QA room, screen target ladder after BAMS Description of setup Duration of setup Installation for experiment duration DAQ & Electronics Software FESA DAQ Trigger Acquire full spill or parts of spill

Experiment Preparation / Required support Estimated amount of time, manpower and equipment

Estimates or simulations Mech. Workshop Beam Line Installation Electronics & DAQ Control System Integration On-site tests Modification of exp. area Dismantling of setup

Remarks & Comments

Investigate: Linearity, absolute calibration, etc.