| Experiment Proposal: AR_2013_No2 |
| --- |
| Title | Author/Spokesperson |
| Test of various types of SEM grids | A. Reiter (1431) B. Walasek-Höhne (1733) |
| Summary & Aim |
| R&D for FAIR: Test of prototype SEM grids Test of DAQ & analogue electronics chain: QFW + FESA-compatible hardware The measurements will be performed with fast and slow extraction from SIS18. Requested beam time: 3 shifts Measured quantities: Beam profile, signal strength and linearity Comparison to other profile measurements (screen, MWPC) Recorded data: Signals as function of particle number, clearing high-voltage |
| Machine parameters |
| Machine SIS18, slow and fast extraction Mode B-exp Exp. area HTP Ion species Light (nitrogen) to heavy ions Beam energy 300 – 800 MeV/u, in principle any Spill length Slow: 300 ms up to 1 second ; Fast: h=4 or h=1 Particle number 104 – 109 per spill Repetition rate ~0.1 Hz or higher Shifts 3 shifts Beam Time Period Autumn 2013 Health & Safety No concerns |
| Experiment procedure |
| After setup of beam at end of HTP line, the following series of data are taken: SEM grid response as function of particle number, beam energy, clearing high-voltage Reference detector at HTP: Ionisation chamber HTPDI1I and SEM HTPDI1S or transformers RT and FCT Test of readout electronics: Charge-to-frequency converter (QFW) with stretcher |

Experiment Setup

Exp. area HTP, new setup of beam line with FAIR standard vacuum chamber. Description of setup Duration of setup Permanent installation DAQ & Electronics Software Long cable to Atomic Physics container, New FESA DAQ Trigger Acquire full spill

Experiment Preparation / Required support Estimated amount of time, manpower and equipment

Estimates or simulations Mech. Workshop Beam Line Installation Electronics & DAQ Control System Integration On-site tests Modification of exp. area Dismantling of setup

Remarks & Comments

Dynamic range, lower detection limit Resolution of SEM grids (Comparison with other detectors) Cross talk effects (clearing electrodes)