| Experiment Proposal: AR_2013_No5 |
| --- |
| Title | Author/Spokesperson |
| Optical Transistion Radiation for Beam Imaging | A. Reiter (1431) B. Walasek-Höhne (1733) |
| Summary & Aim |
| R&D for FAIR: Test of method of beam imaging for heavy ions Feasibility of OTR in proton beam lines towards pBar target Investigation of several types of OTR target foils The measurements will be performed with fast and slow extraction from SIS18. Requested beam time: 10 shifts Measured quantities: Absolute signal, beam profile Comparison with SEM grid and MWPC/IC Test of DAQ & analogue electronics chain with FESA-compatible hardware Recorded data: Signals as function of particle number |
| Machine parameters |
| Machine SIS18, fast extraction Mode B-exp Exp. area HTP Ion species Light and heavy ions Beam energy 300 – 800 MeV/u, in principle any Spill length Slow: 300 ms – 1000 ms Fast: h=4 or h=1 Particle number 104 – 109 per spill Repetition rate ~ 0.1 Hz or higher Shifts 10 shifts, split into 2 campaigns Beam Time Period Autumn 2013, sprint 2014 Health & Safety No concerns |
| Experiment procedure |
| After setup of beam at end of HTP line, the following series of data are taken: Screen signals (beam profiles) for different ion species and energies Investigation of linearity, light yield stability, beta-dependency, q2 dependency |

Experiment Setup

Exp. area HTP beam line Description of setup New FAIR prototype vacuum chamber Duration of setup Chamber: permanent installation OTR setup: May be removed from chamber DAQ & Electronics Software FESA DAQ in Atomic Physics container, New FESA DAQ Trigger Slow extr.: Cycle start - cycle end Fast extr.: Kicker, Flattop reached

Experiment Preparation / Required support Estimated amount of time, manpower and equipment

Estimates or simulations Not required Mech. Workshop Beam Line Installation Electronics & DAQ Control System Integration On-site tests Modification of exp. area Dismantling of setup

Remarks & Comments

Investigate: Linearity, absolute calibration, etc. Use foil at HTP entrance as stripping foil (measurements with two charge-states to test q2 dependency of light yield)