| Experiment Proposal: AR_2013_No6 |
| --- |
| Title | Author/Spokesperson |
| Test of Segmented Ionisation Chamber in Air for pBar Target Monitoring | A. Reiter (1431) M. Witthaus |
| Summary & Aim |
| R&D for FAIR: Test of method of beam imaging for 30 GeV protons Feasibility of segmented air ionisation chamber at pBar target The measurements will be performed with fast and slow extraction from SIS18. Requested beam time: 5 shifts Measured quantities: Absolute signal, beam profile Comparison with SEM grid and MWPC/IC Test of DAQ & analogue electronics chain with FESA-compatible hardware Recorded data: Signals as function of particle number, extraction length |
| Machine parameters |
| Machine SIS18, fast extraction Mode B-exp Exp. area HTP Ion species Light and heavy ions Beam energy 300 – 800 MeV/u, in principle any Spill length Slow: 300 ms – 1000 ms Fast: h=4 or h=1 Particle number 104 – 109 per spill Repetition rate ~ 0.1 Hz or higher Shifts 10 shifts, split into 2 campaigns Beam Time Period Autumn 2013, sprint 2014 Health & Safety No concerns |
| Experiment procedure |
| After setup of beam at end of HTP line, the following series of data are taken: Chamber signals (beam profiles) for light/heavy ion species and different energies Investigation of linearity, light yield stability, dE/dx dependency |

Experiment Setup

Exp. area HTP beam line, dump area Description of setup Pneumatic actuator at end of HTP beam line Duration of setup 2013/2014 measurement campaign No interference with other detectors, if in outer end position DAQ & Electronics Software FESA DAQ in Atomic Physics container, new FESA DAQ (QFW) Trigger Slow extr.: Cycle start - cycle end Fast extr.: Kicker, Flattop reached

Experiment Preparation / Required support Estimated amount of time, manpower and equipment

Estimates or simulations Not required Mech. Workshop 3 days Pneumatic actuator at HTP (special for T-DG090) Adaptation for mounting of detector in drive Beam Line Installation 0.5 days Electronics & DAQ DAQ in Atomic Physics Container, QFW with FESA DAQ system and GUI Control System Integration Not needed! Existing pneumatic actuator control. On-site tests Modification of exp. area Dismantling of setup

Remarks & Comments

Investigate: Linearity, comparison with SEM grid and MWPC profiles