| Experiment Proposal: AR_2013_No1 |
| --- |
| Title | Author/Spokesperson |
| Test of Ionisation Chambers & QFW electronics with Fast & Slow Extraction | A. Reiter (1431) M. Witthaus (2447) |
| Summary & Aim |
| R&D for FAIR: Adaptation of QFW electronics to fast & slow extraction Feasibility of air-IC application in high-radiation environment at pBar Separator The response of an ionisation chambers will be investigated for short beam pulses. These pulses will be produced from SIS18 using fast extraction (h=4 or h=1). Requested beam time: 5 shifts Measured quantities: Signal strength and linearity (comparison/extrapolation to pBar Separator parameters) Test of DAQ & analogue electronics chain: QFW & pulse stretcher Recorded data: Chamber signals as function of particle number, QFW/pulse stretcher parameters and high voltage setting |
| Machine parameters |
| Machine SIS18, fast extraction, h=4 or h=1 Mode B-exp Exp. area HTP Ion species Uranium, Nitrogen Beam energy 300 – 800 MeV/u, in principle any Spill length Slow extraction: 300 ms – 1000 ms Fast extraction: 1 µs extraction; 4 bunches of ~100 ns length each or single bunch (h=1) Particle number 104 – 109 per spill Repetition rate ~0.5 Hz or higher Shifts 5 shifts Beam Time Period Any machine experiment (B-exp) after June 2013 Several measurement blocks Health & Safety No concerns |
| Experiment procedure |
| After setup and optimisation of beam line to HTP, the following series of data are taken: Ionisation chamber responses as function of particle number, ionisation production rate, high voltage setting QFW: minimum detectable signal, linearity Reference detectors at HTP: Ionisation chamber HTPDI1I and SEM HTPDI1S or transformers RT and FCT DAQ test of readout electronics: Charge-to-frequency converter (QFW) and scaler/counter system |

Experiment Setup

Exp. area HTP, beam dump area Description of setup SEM-type ionisation chamber (IC) in air + several LHC-type BLMI + HTPDI1I + FAIR-prototype MWPC/IC Detector positions behind exit of last diagnostics chamber or in beam line (FAIR prototype chamber + HTPDK1) Distance to beam dump: ~ 50-100 cm Test IC with positive and negative HV Duration of setup 2013/2014 measurement campaign DAQ & Electronics Software DAQ setup in Atomic Physics container, signal stretcher (RC-circuit), QFW or IFC converter & Ablass/Lassie FESA system, digital oscilloscope Standard operating software + Java GUI for FESA DAQ Trigger Slow extraction: Cycle start – cycle end (acquire full spill) Fast extraction: Flattop reached

Experiment Preparation / Required support Estimated amount of time, manpower and equipment

Estimates or simulations 1 day Signal estimate A. Reiter Mech. Workshop Not required Beam Line Installation 3 h H. Graf: Remount SEM on pneumatic actuator, alignment Electronics & DAQ 3 days Setup of electronics in DAQ container and tests (A. Reiter / M. Witthaus) Control System Integration 1 day Trigger of Ablass scaler system: Due to pulse stretching acquisition between events [32,55] ??? Window: [flat top, extr.+250 ms] On-site tests Modification of exp. area No Pneumatic actuator in place at HTP 2 RG214 cables to AP container from patch panel Dismantling of setup 2 h Dismount setup, store detector at HTP (A. Reiter)

Remarks & Comments