| Experiment Proposal: AR_2013_No5 |
| --- |
| Title | Author/Spokesperson |
| Screen investigations with fast extraction | A. Reiter (1431) B. Walasek-Höhne (1733) |
| Summary & Aim |
| R&D for FAIR: Test of new SEM grids Investigation of several types of screen materials The measurements will be performed with fast extraction from SIS18. Requested beam time: 6 shifts Measured quantities: Absolute signal, linearity Test of DAQ & analogue electronics chain with FESA-compatible hardware Recorded data: Signals as function of particle number, beam width |
| Machine parameters |
| Machine SIS18, fast extraction Mode Exp. area HTP Ion species Light and heavy ions Beam energy 300 – 800 MeV/u, in principle any Spill length Fast: h=4 or h=1 Particle number 104 – 109 per spill Repetition rate ~ 0.1 Hz or higher Shifts 3 shifts Beam Time Period Autumn 2013 Health & Safety No concerns |
| Experiment procedure |
| After setup of beam at end of HTP line, the following series of data are taken: Screen signals (beam profiles) for different ion species and energies Investigation of quenching, linearity, light yield stability |

Experiment Setup

Exp. area HTP, screen target ladder in front of beam dump Description of setup Duration of setup Permanent installation DAQ & Electronics Software Long cable to Atomic Physics container, New FESA DAQ Trigger Acquire full spill

Experiment Preparation / Required support Estimated amount of time, manpower and equipment

Estimates or simulations Mech. Workshop Beam Line Installation Electronics & DAQ Control System Integration On-site tests Modification of exp. area Dismantling of setup

Remarks & Comments

Investigate: Linearity, absolute calibration, etc.