| Experiment Proposal: AR_2013_No7 |
| --- |
| Title | Author/Spokesperson |
| Plastic Scintillator Response & Test of High-Rate Photomultipliers for FAIR beam loss system | A. Reiter (1431) T. Hoffmann |
| Summary & Aim |
| R&D for FAIR: Test of HW for beam loss monitoring Development of high-rate PMT Scintillator response to minimum- and highly-ionising radiation (core & halo components) The measurements will be performed with slow extraction from SIS18. Requested beam time: 1 shifts Measured quantities: Absolute signal, rate stability of PMT output, pulse-height spectra Test of DAQ & analogue electronics chain with FESA-compatible hardware Recorded data: Signals as function of particle type, count rate and PMT high voltage |
| Machine parameters |
| Machine SIS18, slow extraction Mode B-exp Exp. area HTP Ion species Light, medium and heavy ions (nitrogen, carbon, iron, uranium) Light ions for rate test! Beam energy 300 – 800 MeV/u, in principle any Spill length Slow: 300 ms – 1000 ms Particle number 104 – 109 per spill Repetition rate ~ 0.1 Hz or higher Shifts 3 shift, other measurement in parallel mode Beam Time Period Autumn 2013, sprint 2014 Health & Safety No concerns |
| Experiment procedure |
| After setup of beam at end of HTP line, the following series of data are taken: Scintillator signals for light to heavy ion species and different energies Investigation of linearity, light yield stability, dE/dx dependency |

Experiment Setup

Exp. area HTP beam line, dump area Description of setup Vertical stepper-motor actuator at end of HTP beam line Duration of setup 2013/2014 measurement campaign No interference with other detectors, if in outer end position DAQ & Electronics Software FESA DAQ in Atomic Physics container, new FESA DAQ (QFW) Trigger Slow extr.: Cycle start - cycle end

Experiment Preparation / Required support Estimated amount of time, manpower and equipment

Estimates or simulations Done Mech. Workshop 3 days Pneumatic actuator at HTP Adaptation for mounting of detector in drive Beam Line Installation 0.5 days Electronics & DAQ DAQ in Atomic Physics Container, QFW with FESA DAQ system and GUI NEW FESA class required Control System Integration Not needed! New stepper motor hardware for FAIR including remote operation via GUI. On-site tests Modification of exp. area Dismantling of setup

Remarks & Comments

Investigate: Linearity, dEdx dependency,