| Experiment Proposal: AR_2014_No1 |
| --- |
| Title | Author/Spokesperson |
| Test of standard-size MWPC/IC for FAIR | A. Reiter (1431) |
| Summary & Aim |
| R&D for FAIR: Test of new MWPC/IC detector sandwich The response of an multi-wire proportional chamber and the attached ionisation chamber will be investigated. The measurements will be performed with slow extraction from SIS18. Requested beam time: 2 shifts Measured quantities: Beam profile, signal strength and linearity Comparison to other profile measurements (screen, SEM grid) Test of DAQ & analogue electronics chain: QFW + FESA-compatible hardware Recorded data: Chamber signals as function of particle number, high voltage settings Definition of chamber operation region and estimate of gas gain |
| Machine parameters |
| Machine SIS18, slow extraction Mode B-exp Exp. area HTP Ion species Light and heavy ions Beam energy 300 – 800 MeV/u, in principle any Spill length 300 ms up to 1 second Particle number 104 – 109 per spill Repetition rate ~ 0.1 Hz or higher Shifts 3 shifts Beam Time Period Autumn 2013 Health & Safety No concerns |
| Experiment procedure |
| After setup of beam at end of HTP line, the following series of data are taken: Ionisation chamber response as function of particle number, beam energy, high voltage Reference detector at HTP: Ionisation chamber HTPDI1I and SEM HTPDI1S Test of readout electronics: Charge-to-frequency converter (QFW) and scaler/counter system |

Experiment Setup

Exp. area HTP, new setup of beam line with FAIR standard vacuum chamber. Description of setup Duration of setup Permanent installation DAQ & Electronics Software Long cable to Atomic Physics container, New FESA DAQ Trigger Acquire full spill

Experiment Preparation / Required support Estimated amount of time, manpower and equipment

Estimates or simulations Mech. Workshop Beam Line Installation Electronics & DAQ Control System Integration On-site tests Modification of exp. area Dismantling of setup

Remarks & Comments