| Experiment Proposal: AR_2013_No10 |
| --- |
| Title | Author/Spokesperson |
| Test of MWPC Saturation Effects and Profile Distortions | A. Reiter (1431) B. Walasek-Höhne (1733) |
| Summary & Aim |
| R&D for FAIR: Test of MWPC Saturation and Gas Gain Distortion Investigation of Beam Profile Measurements Measurement of Gas Gain dependency on chamber high voltage The measurements will be performed with slow extraction from SIS18. Requested beam time: 2 shifts Required detectors HTPDI1I and HTPDG1G, Reference screen on target ladder Recorded data: Ionisation chamber current and MWPC profiles as function of particle number in spill |
| Machine parameters |
| Machine SIS18, slow extraction Mode B-exp Exp. area HTP Ion species Light, medium and heavy ions (nitrogen, carbon, iron, uranium) Beam energy 300 – 800 MeV/u, in principle any Spill length Slow: 300 ms – 1000 ms Particle number 104 – 109 per spill Repetition rate ~ 0.1 Hz or higher Shifts 2 shift, other measurement in parallel mode Beam Time Period Autumn 2013, sprint 2014 Health & Safety No concerns |
| Experiment procedure |
| After setup of beam at end of HTP line, the following series of data are taken: Signals of HTPDI1I and HTPDG1G as function of particle number in spill Investigation of IC and MWPC linearity, stability of beam profiles Reference beam profile derived from Cromox screen on target ladder |

Experiment Setup

Exp. area HTP beam line, dump area Description of setup BD components in chamber DK1 Screen on target ladder behind last diagnostics chamber Duration of setup 2013/2014 measurement campaign DAQ & Electronics Software GSI data acquisition for DK1 components BeamView for screen on target ladder Trigger Slow extr.: Cycle start - cycle end

Experiment Preparation / Required support Estimated amount of time, manpower and equipment

Estimates or simulations A. Reiter To be done based on published papers. Mech. Workshop Not required Beam Line Installation Electronics & DAQ DAQ in Atomic Physics Container for BeamView GSI DAQ for HTPDI1I and HTPDG1G Control System Integration On-site tests Modification of exp. area Dismantling of setup

Remarks & Comments

Investigate: Linearity of signal, beam profile distortions, gas gain curve by comparison to reference detectors HTPDI1I and HTPDI1S