| Experiment Proposal: AR_2013_No3 |
| --- |
| Title | Author/Spokesperson |
| Test of new FAIR standard transformer (RT & FCT) | B. Walasek-Höhne (1733) H. Reeg, M. Witthaus |
| Summary & Aim |
| R&D for FAIR: Test of new FAIR beam current transformer combination Response of new transformers (sensor and new amplifier electronics, new DAQ) The measurements will be performed with fast extraction from SIS18. Requested beam time: 5 shifts Measured quantities: Absolute signal, linearity, position dependence of signal Controlled beam steering using profile measurements (screen, MWPC) at HTP Test of DAQ & analogue electronics chain with FESA-compatible hardware Recorded data: Signals as function of particle number, beam position and width |
| Machine parameters |
| Machine SIS18, fast extraction Mode B-exp Exp. area HTP Ion species Light and heavy ions Beam energy 300 – 800 MeV/u, in principle any Spill length Fast: h=4 or h=1 Particle number 104 – 109 per spill Repetition rate ~ 0.1 Hz or higher Shifts 3 shifts Beam Time Period Autumn 2013 or Spring 2014 Health & Safety No concerns |
| Experiment procedure |
| After setup of beam at end of HTP line, the following series of data are taken: Transformer signal as function of particle number, beam energy Charge comparison between FCT and RT Comparison of data to existing RT/FCT (GSI type) at HTP Test of readout electronics |

Experiment Setup

Exp. area HTP, new setup of beam line with FAIR standard vacuum chamber. Description of setup New transformer combination in HTP beam line, mounted in front of existing transformer combination (same beam distribution) Duration of setup Permanent installation DAQ & Electronics Software DAQ setup in Atomic Physics container, New FESA DAQ Trigger Extraction kicker

Experiment Preparation / Required support Estimated amount of time, manpower and equipment

Estimates or simulations Not required Mech. Workshop New transformer must be constructed and installed in HTP beam line (BI dep.) Beam Line Installation YES Electronics & DAQ New amplifiers, optical transmission line (FCT) FESA DAQ for RT & FCT (old and new transformer combinations) Control System Integration Not required On-site tests HW tests by system experts Modification of exp. area Yes, beam line installation Dismantling of setup Not foreseen.

Remarks & Comments

Investigate: Linearity, absolute calibration, position dependence of output signal, comparison to old detector, different time structure (h=1, h=4, different energy) Test transmission via optical link; comparison transmission cable vs. optical link